## Slide 1: Project plan
Stage1 – Inputs:
Knowledge of the infrastructure of the hospital/hospital layout
Survey of the existing waste management practices followed in the hospital
Waste survey in the hospital
Formation of waste management committee
Setting up of Model Ward
Procurement of waste treatment equipment

## Slide 2: Project plan
Stage 2:
Training of staff
Installation of the waste management system
Regular training and awareness for the hospital employees
Monitoring the system

## Slide 3: Flow chart of the work plan
Survey:
Meeting with the heads of all departments
Forming a waste management committee
Rounds of wards to see the functioning
Creating a model ward
Suggest equipment procurement
Formal training for the nursing staff
Implementing the system throughout the
hospital

## Slide 4: Waste management committee
Director and Medical Superintendent
Infection Control Committee head
Representative from Purchase Department
Nursing Supervisor
Housekeeping Supervisor
Representative from Personnel Department
The Committee should meet atleast once in six months and the report must be shared with the prescribed authority as per BMW Rules, 2016

## Slide 5: Waste management policy
Each hospital should have policy that describes:
Steps taken to comply with the Rules
Waste categorisation
Staff’s training content and status
Policy adopted on segregation, collection, transport and storage of waste
Names and duties of waste management committee members
Immunisation status of staff
Format of accident reporting and follow ups
Overall monitoring formats of the system

## Slide 6: Occupational safety and health plan: a step towards safety
Requisite training
Protective gear-should ensure safety, should be well fitting and easy to use, to ensure usage
Safe work practices
Administrative controls
Immunisation of the entire staff against Hepatitis B (mandatory) and tetanus (SOS)
Monitoring and evaluation of work practices

## Slide 7: Why do a waste audit?
Helps in classification of waste
Avoids and helps rectify over-classification
Highlights area specific problems/needs
Reflects on the level of segregation
Possibility of exploring waste minimisation
Scopes of economic gains
Helps locate points of intervention/need based solutions
Subsequent evolution of best practices

## Slide 8: Setting up a model ward
Choosing a ward
Imparting training to all its staff
Implementing the system: segregation of waste, disinfection of infected plastic waste and sharps management
Monitoring and suggesting corrective measures
Implementing the system in the entire hospital

## Slide 9: Components of hospital waste management
Training and awareness of hospital staff
Initiating segregation of waste
Disinfection and mutilation
Secure storage and transportation of waste
Sharps and hazardous waste management
Final treatment and disposal
Monitoring of the system

## Slide 10: Segregation
Different types of waste should be collected separately
Should be done at the point of generation
Different colored bins used to make it easy
Segregation ensures occupational health safety
Segregation also reduces the cost of treatment and disposal

## Slide 11: Segregation: make a difference
Tips to ensure good segregation:
Optimum number of bins; neither less nor more
All bins equally easy to use in terms of handling and placement
Clean bins
Easy operation
Different coloured bins for each category of waste
Proper labeling of bins
Posters in the work area as a constant reminder

## Slide 12: Disinfection and mutilation
Decentralized:
Chemical disinfection: bleach is a good disinfectant
WHO recommended concentration 1% solution (10gms of bleach in 1 litre water) for 30 minutes
Centralized:
Autoclave, microwave, hydroclave for Microbiological and Biotechnological waste
Mutilation:
Mutilation to avoid illegal reuse

## Slide 13: Collection
Some thumb rules for collection:
Designate different people for collection of each type of waste
Collection time preferably different
Collection bins properly labelled and different for each category
Collection in closed containers
Trolleys to be provided for movement
Protective gear is a must during collection

## Slide 14: Storage
Rules prohibit storage of waste beyond 48 hrs
Storage site:
Should have proper warning in front
Should be accessible by vehicles
Should not be accessible to animals or visitors
Should be covered and lockable
The surface should be cleanable
Should have water and electricity supply
Proper drainage outlet

## Slide 15: Transport
Avoid patient/crowded areas
Avoid using lifts meant for patients and/or movement of sterile equipment
Selection of time important-Select time of minimum movement (Not while doctors are on rounds; Not during visiting hour)
Preferably use the hospital ramp
Ergonomics to be taken into consideration: avoid lifting, prefer trolleys
Waste bags should be sealed or tied properly
Hazardous and non-hazardous waste should be carried in separate vehicles

## Slide 16: Waste movement
WARD/
NURSING
STATION
INFECTIOUS
WASTE
YELLOW BAG
ONE PERSON
DESIGNATED
PICKED
ONCE
BAGS
COLLECTED
IN A TROLLEY
WITH A BIN
INCINERATED
PLASTIC
WASTE
Red Bag
ONE PERSON
DESIGNATED
PICKED
ONCE
DISINFECTED IN
WARDS & THE
BAGS TAKEN
IN A LARGE BIN
MUTILATED
GIVEN TO A
CONTRACTOR
GENERAL
WASTE
BLACK
BAG
WARD BOY
PICKED
TWICE
BAGS TAKEN
TO A CENTRAL
POINT
BY WARD BOYS
MUNICIPAL
BIN,
PIGGERY
SHARPS
White/Translucent Puncture proof bag
ONE PERSON
DESIGNATED
PICKED
ONCE
DISINFECTED IN
WARDS, CONTENTS
SIEVED &
COLLECTED IN A BUCKET
COLLECTED
IN THE
HOSPITAL

## Slide 17: Special cases
Operation theatre
Laboratory
Emergency
Nursing station
Kitchen
Laundry

## Slide 18: Monitoring
Monitoring on a daily basis:
Monitoring of the system by sister in charges and senior hospital personnel
Monitoring sheets to be filled up
Take up waste survey before and after establishing the system
Report findings to department heads

## Slide 19: Keep score!
Review every bill from waste vendors
Track monthly waste totals comparing to patient census, outpatient and inpatient procedures

## Slide 20: Conduct routine waste assessment
Note variations and recommendations
  Staff participation in accurate segregation
  Effectiveness of collection schedules
  Adequacy of containers
  Errors in disposal
Offer assistance to rectify problems

## Slide 21: Graph it!

## Slide 22: Graph it!

## Slide 23: Waste Monitoring Sheet

## Slide 24: Economics of waste management
Treatment technology:
Technology option/size of the facility (central facility economically viable)
Equipment:
Needle destroyers, scissors and forceps, bread box, bins
Chemical disinfectant
Protective clothing:
Boots, gloves, face mask, glasses
Different colored bags:
Size, quantity and quality

## Slide 25: Problems faced
Doing the initial trainings at the work place
Changing the attitude of the staff- the initial attitude can be really cold but over the time they appreciate the system
Deciding the equipment for waste management: every place has its own needs and thus procurement can be difficult. Start working on equipment immediately after waste audit and before training

## Slide 26: Lessons learnt
Initial training sessions should not be carried out at the work place
Purchasing of equipment takes time- should be decided before starting trainings
While planning the scheme, time should be kept for factors such as purchasing and staff availability
Model Ward should be set up as a pilot system

## Slide 27: Reduce, reuse, recycle
Sold for recycling (by the CBWTF): Glass (I.V. bottles, ampoules, etc.)
  Paper and cardboard
  Disinfected and mutilated plastics
  Discarded linen for paper recycling
  X-ray films
  Photographic developer
Kitchen waste sent to piggery
Garden waste composted

## Slide 28: Waste minimisation
Segregation
Source reduction
Substitute hazardous processes/substances
Reducing losses by good practices
Preferential purchases
Resource recovery and recycling
Treatment
Proper disposal