## Slide 1: Managing special wastes
Segregation: colour coding
Disinfection
Sharps management
Hazardous waste
  Mercury
  Glutaraldehyde
  Cytotoxic drugs
  Pharmaceuticals
  Radioactive waste

## Slide 2: Categories and colour codes for waste segregation
Waste category | Colour code | Treatment
Human anatomical waste | Yellow (Y) | Inc./ Plasma Pyrolysis/burial
Animal waste | Yellow | Inc./ Plasma Pyrolysis/burial
Soiled Waste | Yellow | Inc./ Plasma Pyrolysis/burial
Discarded Medicines, Cytotoxic drugs | Yellow | Inc./Send back to manufacturer
Microbiology & biotechnology waste | Yellow | Inc. (after lab pre treatment)

## Slide 3: Categories and colour codes
Waste category | Colour code | Treatment
Chemical waste | Yellow | Inc./Plasma Pyrolysis/ HSDF
Chemical Liquid waste | – | Resource Recovery; Pretreatment; discharge
Discarded/contaminated linen, mattresses etc. | Yellow | Non-chlor. Chemical disinfection; inc./Plasma Pyrolysis
Contaminated/Recyclable Waste | Red | Auto/hydroclaving/microwaving; shredding; recycling

## Slide 4: Categories and colour codes
Waste category | Colour code | Treatment
Waste Sharps | White/ translucent (puncture proof) | Autoclave/Shredding; landfill
Glassware (expect Cytotoxic contaminated) | Blue Cardboard boxes | Disinfection/auto/hydroclaving/microwaving; recycling
Metallic Body Implants | Blue Cardboard boxes | -

## Slide 5: Waste segregation system
Yellow | Red | Blue | White
Human tissues, organs, body parts, animal waste, soiled waste, pharmaceuticals, cytotoxic drugs, chemical, microbiological & biotechnological waste | Contaminated (recyclable) waste | Glassware and metallic body implants | Sharps waste

## Slide 6: Only 15-20% of hospital waste is infectious/hazardous
Segregate waste, it helps:
In infection control
Reduces the hazards associated with infectious waste
Avoids hazards caused by improper treatment eg. Incineration of PVC, mercury or other chemicals
Saves money spent in treatment
Avoids illegal reuse
Decreases occupational hazards
Favours recycling
Fulfills requirement of law

## Slide 7: Segregation – making a difference
Tips to ensure good segregation:
All bins equally easy to use: in terms of handling and placement
Optimum number of bins: neither less nor more
Clean bins
Easy operation
Different coloured bins for each category of waste
Proper labelling of bins
Posters in the work area as a constant reminder

## Slide 8: Chemical disinfection
1% Sodium hypochlorite or an equivalent solution
Minimum residency time of 30 min.
Freshly prepared solution
Accurately made concentration
10% solution in case of heavily soaked material/spill

## Slide 9: Cleaning up a body fluid spill
Have a separate mop for spill clean up:
Clean the spill either with absorbent cotton and discard it in red bin, or clean with the spill mop (reusable after disinfection in a separate bucket)
Now put disinfectant solution on this area and leave it for 10 minutes. Preferably use phenolic agents on floors, or 10% bleaching solution. Wipe with clean mop

## Slide 10: Sharps management: reducing stick injuries
Identify the devices and circumstances in which injuries occur.
Maintain records of stick injuries
Personnel involved and area | Procedure | Type of injury | Device used | Conditions/ circumstances

## Slide 11: Evolving sharps management
Risk area identification
During operations: by suture needles, passing sharps directly in hands
Sharp left unattended
Undestroyed sharp
Sharps in the wrong container
Unsealed sharps container
Puncture prone container

## Slide 12
Studies and follow ups
Study: one-third injuries being caused by recapping
Follow up: Do not recap
One layer of surgical gloves appears to decrease the volume of blood injected by solid suture needles by 70%
Follow up: Follow universal precautions
Evolving sharps management

## Slide 13: Health is wealth: manage sharps
Always wear gloves: one layer of surgical gloves appears to decrease the volume of blood injected (amount of innoculum) by solid suture needles by 70%
Destroy needles, cut syringes using needle destroyer
All sharps to be stored in a puncture resistant container
Sharps should not be transferred in hands
Prohibit recapping
Vaccination of all personnel against HBV
Start PEP in hospitals

## Slide 14: Needle-stick bill
The U.S. Senate unanimously approved new workplace regulations that will dramatically lower the number of potentially lethal needle sticks.
The bill is called the Needle stick Safety and Prevention Act
The legislation will require healthcare facilities nationwide to provide their employees with syringes and blood
Drawing devices incorporating safety features that retract, blunt or cover the needles after they are used.
Studies show that the safety features can reduce accidental needle injuries by up to 80 percent

## Slide 15: Mercury spill management containment kit
Nitrile gloves or two pairs of latex gloves
Face mask
Protection for the eyes
Scotch tape
10 cc syringe
Covered plastic/glass container with water
Posters depicting the process of mercury containment

## Slide 16: Mercury spill: thumb rules
Never touch mercury with bare hands
Wear all protective gears
Gather mercury using stiff paper and suck it in a eyedropper/syringe without the needle
Pour contents of the syringe in a bottle containing water
Put scotch tape around the bottle
Keep the syringe for further use

## Slide 17: Mercury spills: some facts
A thermometer may have 1gm of mercury and a sphygmomanometer, around 85-95gms
As much as 80% of inhaled mercury may be absorbed in the blood stream and the biological half-life of this is around 60 days
1gm of mercury is enough to contaminate a lake of 20 acres
Mercury vapour levels in the BP apparatus monitoring and calibrating stations may sometimes reach the ceiling value of 1mg/10m3 as established by OSHA.

## Slide 18: Mercury spills: some facts
A nurse may take 15 minutes to 12 hours to properly clean up a spill
The room would need to be sealed and cleaned
Cost of spill kits (including good protective gear) is $ 5-200
In Minnesota it was estimated that it costs $ 2,500- 3000 to remove one pound (0.4538kg) of mercury from a municipal waste incinerator’s air emissions

## Slide 19: Spill cleanup guidelines
Ontario Ministry of Labor’s cleanup guidelines:
Written policy and procedures for cleanups
Policy to be posted at all work places
Training of staff on method of cleanups and use of protective gear

## Slide 20: Minor spills
Small spills can be cleaned up with a vacuum cleaner equipped with charcoal filter or water trap
Surfaces should then be washed with mercury neutralising solution (like 20% calcium sulphide or 20% sodium thiosulphate)
Sulphur powder can be sprinkled over the area immediately after spill to avoid mercury vapourisation (till cleaning up)

## Slide 21: Glutaraldehyde safety action plan
Identify all usage locations
Monitor exposure levels
Training
Use personal protective equipment
Administrative controls
Work practice controls
Engineering controls
Neutralise solution before discarding
Develop a spill cleanup plan

## Slide 22: Cytotoxic waste
Disposal:
Disposed of either by incineration/Plasma Pyrolysis/Encapsulation at CBWTF of HSDF site or send back to the manufacturer.
Cleanup of small spills:
5ml or 5g outside a hood should be wiped with absorbent gauze and then cleaned (thrice) with detergent and water. Any glass fragments should be placed in a cardboard or plastic container and then into a CD disposal bag, along with used absorbent pads. Glassware or other contaminated reusable items should be placed in a plastic bag and washed with detergent

## Slide 23: Spill kits
Ready to use kits
Labeled and kept in or near preparation or administrative areas.
Kits should include: a respirator, chemical splash goggles, two pairs of gloves, two sheets (12x12) of absorbent material, 250-ml and 1-litre spill-control pillows, and a small scoop to collect glass fragments. Finally, the kit should contain two large CD waste-disposal bags.

## Slide 24: Larger spills
Cover spill with absorbent sheets. Damp cloth should be used if powder is involved. Care must be taken not to generate aerosols; restrict access to spill.
Use respirators when there is danger of airborne powder or aerosols.
Chemical in activators should not be applied to the absorbed drug as it may produce hazardous by-products. (However, sodium thiosulfate can be safely used to inactivate nitrogen mustard.)
All contaminated surfaces should be thoroughly cleaned with detergent and then wiped with clean water. Contaminated materials should be disposed of in the CD disposal bag

## Slide 25: Direct contact with CDs
The following actions, as appropriate, should be taken for overt contamination by cytotoxic agents:
Immediately change the contaminated gloves or gown.
Immediately wash the affected skin area with soap and water and have a physician examine the area as soon as possible.
Immediately flood the affected eye with eyewash designated for that purpose; seek medical attention immediately.
Report incidents involving skin or eye contact in accordance with hospital procedure

## Slide 26: Contaminated laundry
Shall be handled as little as possible with minimum agitation
Bagged at the location where it was used and shall not be sorted or rinsed in the location of use
Placed and transported in labeled bags or containers
If wet and presents a reasonable likelihood of soak-through, the laundry shall be placed and transported in bags or containers which prevent leakage of fluids
Ensure that employees who have contact with contaminated laundry wear protective gloves and other appropriate personal protective equipment

## Slide 27: Follow up meeting with trainees
Interactive session: what is being practiced?
Problems faced, if any, with segregation, equipment
Enlist problems from your monitoring sheets
Answer to queries, if any