## Slide 1: Overview
Bio-medical Waste Management Rules, 2016
The Rules apply to all persons who generate, collect, receive, store, transport, treat, dispose or handle bio-medical waste in any form
The rules have been notified under the Environment (Protection) Act, 1986
First draft in 1995, Second draft in 1997
Final rules notified on July 27, 1998
First Amendment in March, 2000; Second amendment in June, 2000; Third amendment in Sept, 2003
Revised Final Rules came in March, 2016
Supported by three guidelines

## Slide 2: Important definitions
Bio-medical waste:
Any waste which is generated during the diagnosis, treatment, or immunization of human beings or animals or research activities or in the production or testing of biologicals or in health camps, including categories mentioned in Schedule 1
Occupier:
A person who has control over an institution (and/or its premises) which is generating bio medical waste

## Slide 3: Important definitions
Authorisation:
Means permission granted by the prescribed authority for the generation, collection, reception, storage, transportation, treatment, disposal and/ or any other form of handling of bio- medical waste in accordance with the rules
Bio-medical waste treatment and disposal facility:
Any facility wherein treatment, disposal of bio-medical waste or processes incidental to these are carried out and includes common bio medical waste treatment facilities

## Slide 4: Provisions and clauses
Duty of occupier: to ensure that bio-medical waste is handled without any adverse effect to human health and environment
Treatment and disposal
  In accordance with Schedule I and in compliance with standards in Schedule II. Facility off- site
  Segregation, packaging, transport and storage
  Bio-medical waste shall not be mixed with any other waste
  Shall be segregated at the point of generation as per the colour codes in Schedule I.

## Slide 5: Provisions and clauses
Containers should be appropriately labeled and bar coded
Transportation only in authorized vehicles with installed GPS.
No untreated waste shall be stored beyond 48 hrs, incase of emergency permission must be sought from prescribed authority
Municipal authorities shall continue to pick up and transport segregated non bio-medical waste from healthcare facilities.

## Slide 6: Prescribed authority
State Pollution Control Board/Committee
Applications for seeking authorisation to be disposed within 90 days
The authority may after giving reasonable opportunity of being heard to the applicant and for reasons thereof to be recorded in writing, refuse to grant/renew authorisation
May cancel/suspend an authorization in case of non- compliance of rules by operator/occupier. Suspension/cancellation of authorisation, only after opportunity to the applicant to be heard, reasons to be recorded in writing
Appeal against the order by the applicant within 30 days

## Slide 7: Authorisation
The authorisation will be one time for non-bedded occupier
Bedded occupiers will apply for authorisation as per Form II.
Authorisation to operate a facility would be issued in Form III
The validity of the authorisation will be synchronized with the validity of consents.

## Slide 8: Records
Annual reports
Details of category and quantity of waste handled, mode of treatment with details. Submission to Prescribed Authority by June 30
Maintenance of records
Records related to generation, collection, reception, storage, transportation, treatment, disposal or any other from of handling of bio- medical waste. Subject to inspection and verification at any time
Accident Reporting
Any accident during handling or transportation of bio- medical waste should be reported to the Prescribed Authority in Form I

## Slide 9: Schedule I:
Waste category | Colour code | Treatment
Human anatomical waste | Yellow | Inc./ Plasma Pyrolysis/burial
Animal waste | Yellow | Inc./ Plasma Pyrolysis/burial
Soiled Waste | Yellow | Inc./ Plasma Pyrolysis/burial
Discarded Medicines, Cytotoxic drugs | Yellow | Inc./Send back to manufacturer
Microbiology & biotechnology waste | Yellow | Inc. (after lab pre treatment)

## Slide 10
Waste category | Colour code | Treatment
Chemical waste | Yellow | Inc./Plasma Pyrolysis/ HSDF
Chemical Liquid waste | – | Resource Recovery; Pretreatment; discharge
Discarded/contaminated linen, mattresses etc. | Yellow | Non-chlor. Chemical disinfection; inc./Plasma Pyrolysis
Contaminated/Recyclable Waste | Red | Auto/hydroclaving/microwaving; shredding; recycling

## Slide 11
Waste category | Colour code | Treatment
Waste Sharps | White/ translucent (puncture proof) | Autoclave/Shredding; landfill
Glassware (expect Cytotoxic contaminated) | Blue Cardboard boxes | Disinfection/auto/hydroclaving/microwaving; recycling
Metallic Body Implants | Blue Cardboard boxes | -

## Slide 12
Colour Coding | Type of container
Yellow | Non chlorinated plastic bag
Red | Non chlorinated plastic bags or containers
Blue | Cardboard boxes with blue colored marking
White(Translucent) | Puncture proof, Leak proof, tamper proof containers
Schedule I: Colour coding

## Slide 13: Take note
No storage of untreated waste beyond 48 hrs
No incineration of chlorinated plastics, no chemical pretreatment before incineration
Bags for collecting any category of Bio-Medical waste should not be made of chlorinated plastic.
Labeling and bar coding of waste
Label shall be non-washable and visible
Deep burial option
Inclusion of new technologies

## Slide 14: Role of municipal body
Municipal body to continue to pick up and transport segregated non- biomedical waste and treated medical waste

## Slide 15: Role of Prescribed Authorities
MOEF & CC is the prescribed authority to make policies concerning Bio medical waste and is responsible to provide financial assistance for setting up or up gradation of CBWTF.
It will also review the implementation of the rules once a year through SPCBs and CPCB.

## Slide 16: Incineration standards
Combustion Efficiency at least 99%
Temperature
  Primary Chamber-800+/-50oC
  Secondary Chamber- 1000+/-50oC
Secondary chamber gas residence time at least 2 seconds, with minimum 3% oxygen in the stack gas
Minimum Stack height shall be 30 meters above ground

## Slide 17: Incinerator
Chlorinated plastics cannot be incinerated
No chemical Pretreatment before incineration
Low sulphur fuel to be used
Toxic metal limit in ash, as specified in Hazardous Waste Rules

## Slide 18: Environment Protection Act, 1986
Section 5: Powers to give directions
Section 6: Rules to regulate environmental pollution
Section 8: Persons handling hazardous substances to comply with procedural safeguards
Section 10: Powers of entry and inspection
Section 11: Powers to take samples...

## Slide 19: Environment Protection Act, 1986
Section 15: Penalty for contravention of the provisions of the Act and the rules, orders and directions
Section 16: Offences by Companies
Section 17: Offences by Government Departments
Section 22: Bar of jurisdiction

## Slide 20: Associated rules
Environment Protection Act, 1986
Solid Waste (Management and Handling) Rules, 2016
Atomic Energy Act
Hazardous Wastes (Management & Handling) Rules, 1989
E-Waste (Management and Handling) Rules, 2011